## Slide 1: Control Hardware in the Loop of Voltage Source Converters (VSCs)
SUNRISE Summer School
Belgrade 10-13/9/2024
Manuel Barragán Villarejo
Department of Electrical Engineering
University of Sevilla
(manuelbarragan@us.es)

## Slide 2: Outline
General overview of Typhoon HIL
Schematic Editor
HIL SCADA
Interface Typhoon-HIL 402 to DSP TMS320F28335
DSP TMS320F28335
Code composer studio
Description of the main.c file in CCS
Selection of control parameters

## Slide 3: General overview of Typhoon HIL 402/404
Functionalities:
  Real time simulation
  Control Hardware in the Loop: C-HIL
  Power Hardware in the Loop: P-HIL
Hardware:
  Real time platform
  HIL DSP Interface
  DSP
Software:
  Schematic editor
  HIL Scada
  Typhoon Test
  Typhoon RCP

## Slide 4: Schematic Editor

## Slide 5: HIL SCADA
https://www.typhoon-hil.com/documentation/typhoon-hil-api-documentation/typhoon_api.html#
https://www.typhoon-hil.com/documentation/typhoon-hil-software-manual/References/action_widgets.html

## Slide 6: Interface Typhoon-HIL 402/404 to DSP TMS320F28335
DSP Interface
Analog signal connector
Digital signal connector
DIM100 control card connector
SPI (Serial Peripheral Interface) DAC
CAN bus
XDS100v2 and UART

## Slide 7: Interface Typhoon-HIL 402/404 to DSP TMS320F28335
DSP Interface
Analog signal connector
Buffer ADC. CCS
03
02
00
09
10
11
01
04
05
06
07
08

## Slide 8: Interface Typhoon-HIL 402/404 to DSP TMS320F28335
DSP Interface
Digital signal connector
PWM: Top phase A
PWM: Bottom phase A
PWM: Top phase B
PWM: Bottom phase B
PWM: Top phase C
PWM: Bottom phase C
Enable DC
Enable AC
PWM: Top DC/DC
PWM: Bottom DC/DC
Interrupt

## Slide 9: DSP TMS320F28335
Up to 150 MHz (6.67-ns cycle time)
On-chip memory: 256K × 16 flash, 34K × 16 SARAM
Peripherals: 3.3-V I/O design
  Up to 18 PWM outputs
  12-bit ADC, 16 channels
  Up to 88 individually programmable, multiplexed GPIO pins with input filtering
Serial port peripherals
  Up to 2 CAN modules
  Up to 3 SCI (UART) modules
https://www.ti.com/lit/ds/symlink/tms320f28335.pdf?ts=1725436907130&ref_url=https%253A%252F%252Fdev.ti.com%252F

## Slide 10: Code composer studio
Code Composer Studio is an integrated development environment (IDE) for TI's microcontrollers and processors. It comprises a suite of tools used to develop and debug embedded applications.
Includes an optimizing C/C++ compiler, source code editor, project build environment, debugger, profiler and many other features
Compilers for proprietary architectures such as MSP430TM, C2000TM and DSPs are included as well as a compiler for Arm®-based microcontrollers
*Presentation installation_CCS provided contains the details for installation and configuration of CCS

## Slide 11: Description of the main.c file in CCS
DSP initialization and configuration is performed
VSC control functions are executed
From Line 1 to Line 63.
  Libraries
  Functions for configuring peripherals
  ADC Conversion
  PLL & Park transformation functions
  Fault State Machine (FSM)
  Control functions based on PLL:
  Control functions based on VSG:
  Auxiliary computations
  Global variables

## Slide 12: Description of the main.c file in CCS
From Line 66 to Line 141. ‘main’ function
  DSP Initialization
  Initialization of the flash memory
  Clock frequency definition
  GPIOs Initialization and Configuration
  Interrupts Initialization
  DMA Initialization
  ADC Initialization
  ePWM Initialization

## Slide 13: Description of the main.c file in CCS
From Line 143 to Line 151. ADC interruption 1 for ADC
From Line 154 to Line 225. ADC interruption 1 for control loop
  GIPO12 for enabling switching the VSC
  Calibration. Input ADC_read. Analog channels reading
  RMS computation. Input ADC converts to Volts and Amps
  power computation
  PLL and Park transformation
  State machine
  Enable/disable ePWM
  Controller selection
  Carrier based PWM
  Reinitialize for next ADC sequence

## Slide 14: Description of the main.c file in CCS
File ‘State_machine.c’. Function state_mac. Table with type of Faults

## Slide 15: Description of the main.c file in CCS
Controller selection
Function DQCURRENT_comp dq current controller
Function DQCURRENT_comp dq power controller
Function DQSTATCOM_comp dq statcom controller
Function VSG_comp dq vsg controller

## Slide 16: Selection of control parameters
Header file: type_structs.h
  PWM timer
  Dead-band PWM
  Execution rate of the controller
  Device to which the dsp connects
  Number of wires of the VSC
  Controller selection
  Synchronization of the DSP
  Enabling the state machine
  ADC calibration
  Limits of operation of the VSC
  Controller gains
  Structures: They are a way to group several related variables into one place

## Slide 17: Outline
General overview of Typhoon HIL
Schematic Editor
HIL SCADA
Interface Typhoon-HIL 402 to DSP TMS320F28335
DSP TMS320F28335
Code composer studio
Description of the main.c file in CCS
Selection of control parameters

## Slide 18: Control Hardware in the Loop of Voltage Source Converters (VSCs)
SUNRISE Summer School
Belgrade 10-13/9/2024
Manuel Barragán Villarejo
Department of Electrical Engineering
University of Sevilla
(manuelbarragan@us.es)