## Slide 1: Modeling and control of Voltage Source Converters (VSCs) Part II
SUNRISE Summer School
Belgrade 8-11/7/2025
Manuel Barragán Villarejo
Department of Electrical Engineering
University of Sevilla
(manuelbarragan@us.es)

## Slide 2: Outline
Introduction
Three-phase inverter
Pulse Width Modulation (PWM)
Coupling filter
Averaged model of Three-Phase Three-wire Two-level VSC in abc
Averaged model of Three-Phase Three-wire Two-level VSC in dq
Grid synchronization: Phase Lock Loop (PLL)
VSC control
Current control in dq coordinates
Computation of reference current
DC-link voltage control

## Slide 3: VSC control
Hierarchical controller of the VSCs
LOW LEVEL CONTROL
PWM and current controller
MID LEVEL CONTROL
P-Q Control: GFL or GFM
DC bus voltage control
HIGH LEVEL CONTROL
Primary frequency control
Voltage control
Power Smoothing
EMS of ESS
Notes: In this scenario, VSCs, the main interface between renewable generation and the electrical system, have a very important role thanks to their control capacity. They can provide a series of ancillary services, which, together with energy storage systems, can address many challenges.
In this way, it is necessary to propose a control scheme that allows providing the different auxiliary services in the time range that corresponds to them, from services with very fast dynamics: electromagnetic flames to those whose dynamics are slower and classically characteristic of power systems.

## Slide 4: VSC control
Variables to be controlled:
  DC voltage:
  Currents:
Inputs:
Subactuated control system: 3 inputs to control 4 outputs
Take advantage of the different dynamics of the control scheme
  Low level: Current controller:
    Fast dynamics
    Usual time constant: 1-10 ms
  Mid level: DC voltage controller:
    Slow dynamics
    Usual time constant: 10-100 ms
Current regulator
DC voltage regulator
+
+

## Slide 5: Current control in dq coordinates
AC-side equivalent model in dq:

## Slide 6: Current control in dq coordinates
Auxilary variables: and

## Slide 7: Current control in dq coordinates
PI current controller
Transfer function to be controlled

## Slide 8: Current control in dq coordinates
Relationship auxiliary and actual inputs
Actual Inputs computation: and

## Slide 9: Current control in dq coordinates

## Slide 10: Current control in dq coordinates
Tuning of the controller gains
Desired 1st order
closed-loop dynamics
Block Algebra
Open Loop
Transfer function

## Slide 11: Current control in dq coordinates
Tuning of the controller gains
Block Algebra
Closed Loop
Transfer function
Identifying with the desired closed-loop dynamic
;

## Slide 12: Methodology
✓
Plant
Control
SCADA
Notes: In this scenario, VSCs, the main interface between renewable generation and the electrical system, have a very important role thanks to their control capacity. They can provide a series of ancillary services, which, together with energy storage systems, can address many challenges.
In this way, it is necessary to propose a control scheme that allows providing the different auxiliary services in the time range that corresponds to them, from services with very fast dynamics: electromagnetic flames to those whose dynamics are slower and classically characteristic of power systems.

## Slide 13: Computation of reference currents
Active and reactive power in abc coordinates:
Matrix formulation in abc coordinates:
Active and reactive power in dq coordinates:

## Slide 14: Computation of reference currents
Active and reactive power in dq coordinates (matrix form):
Current references in dq coordinates:

## Slide 15: DC-link voltage control
DC-side equivalent circuit in abc and dq:
Power balance between AC and DC side of the VSC

## Slide 16: DC-link voltage control
PI regulator provides the active power reference to maintain :
PI
regulator
Perturbation
dq current
reference computation
PI
Current controller
Plant

## Slide 17: Computation of reference currents
DC-link voltage and current control

## Slide 18: Methodology
✓
Plant
Control
SCADA
Real Time Simulation
Real-Time Simulator
Host
PC
✓
Notes: In this scenario, VSCs, the main interface between renewable generation and the electrical system, have a very important role thanks to their control capacity. They can provide a series of ancillary services, which, together with energy storage systems, can address many challenges.
In this way, it is necessary to propose a control scheme that allows providing the different auxiliary services in the time range that corresponds to them, from services with very fast dynamics: electromagnetic flames to those whose dynamics are slower and classically characteristic of power systems.

## Slide 19: Methodology
✓
Plant
Control
SCADA
C-HIL
Host
PC
Real-Time Simulator
DSP
✓
Notes: In this scenario, VSCs, the main interface between renewable generation and the electrical system, have a very important role thanks to their control capacity. They can provide a series of ancillary services, which, together with energy storage systems, can address many challenges.
In this way, it is necessary to propose a control scheme that allows providing the different auxiliary services in the time range that corresponds to them, from services with very fast dynamics: electromagnetic flames to those whose dynamics are slower and classically characteristic of power systems.

## Slide 20: Outline
Introduction
Three-phase inverter
Pulse Width Modulation (PWM)
Coupling filter
Averaged model of Three-Phase Three-wire Two-level VSC in abc
Averaged model of Three-Phase Three-wire Two-level VSC in dq
Grid synchronization: Phase Lock Loop (PLL)
VSC control
Current control in dq coordinates
Computation of reference current
DC-link voltage control

## Slide 21: Modeling and control of Voltage Source Converters (VSCs) Part II
SUNRISE Summer School
Belgrade 10-13/9/2024
Manuel Barragán Villarejo
Department of Electrical Engineering
University of Sevilla
(manuelbarragan@us.es)